## Slide 1
A Smart Patient Monitoring System for Improved Healthcare
Supervisor
MOHAMMAD MAMUN ELAHI
Assistant Professor
DEPT OF CSE,UIU
Course Teacher
A.K.M. Muzahidul Islam Professor
DEPT OF CSE,UIU
GROUP C-1
Group Members
Abdullah Al Mamun ID: 011 161 186
Dill Mahzabina Tabila ID: 011 161 274
Md. Fanir-Al-Mamun ID: 011 161 142
Sanjida Akter Shimu ID: 011 161 195
Khandakar Sharmin Sara ID: 011 161 197
Sifullah Sajib ID: 011 161 185

## Slide 2
Introduction
  Project Overview
  Problem Statement
  Objective
  Motivation
  Research Framework
Literature Review
Methodology
  Proposed System Architecture
  Software Requirements
  Hardware Requirements
Expected Outcomes
Implementation
Standards and Design Constraints
Gantt Chart
Conclusion and Future Work
References
Content
United International University

## Slide 3
United International University
Introduction
Project Overview:
  Develop a cloud-based Smart Patient Monitoring System using Internet of Things (IoT).
  Collect patient data through sensors and monitor through a centralized web-based application.
  Pre-process the collected data and decide which data to forward to the cloud for user (doctors/attendants) apps.

## Slide 4
Objective:
  To design a system for collecting a patient's body status at regular intervals through sensors.
  To develop an web-based application to monitor critical patient conditions 24/7.
  To provide a common platform for efficient interaction between patients and doctors.
Problems in Existing Healthcare System & Motivation:
  Shortage of medical personnel.
  Hospital system mismanagement.
  Inexperienced new medical personnel.
  Medical personnel absenteeism.
Introduction (contd.)
United International University

## Slide 5
Research Framework
Figure 1: Research Framework
Introduction (contd.)
United International University

## Slide 6
Chao Li, Xiangpei Hu, and Lili Zhang. The iot-based heart disease monitoring system for pervasive healthcare service. Procedia computer science, 112:2328-2334, 2017.
  This system sends patient's physical sign to remote medical applications in real-time.
  Data acquirement part and data dispatch.
  Heart disease monitoring system.
  SpO2 sensor device and android mobile phone for getting notification.
S Gowrishankar, MY Prachita, and Arvind Prakash. Iot based heart attack detection, heart rate and temperature monitor. International Journal of Computer Applications, 170(5):26-30, 2017.
  This system senses and monitors pulse rate and body temperature.
  Three major modules: the sensing module, the main module, and the interaction module.
  Established a gateway between the sensor node and the brain node.
  Temperature sensor LM35 and pulse sensor.
  HTTP communication protocol.
Literature Review
United International University

## Slide 7
Vikas Vippalapalli and Snigdha Ananthula. Internet of things (iot) based smart health care system. In 2016 International Conference on Signal Processing, Communication, Power and Embedded System (SCOPES), pages 1229-1233. IEEE, 2016.
  Body temperature and blood pressure.
  Arduino Fio, temperature sensor, blood pressure and pulse sensor.
  The Sphygmomanometer measures blood pressure.
  Visualized by LabView software which used TELNET protocol.
JV Alamelu and A Mythili. Design of iot based generic health care system. In 2017 International conference on Microelectronic Devices, Circuits and Systems (ICMDCS), pages 1-4. IEEE, 2017.
  A wireless sensor network in an IoT environment with cloud computing.
  Using a gateway to monitor the base station.
  Blood sugar sensor, heart pressure sensor, weight scale sensor.
Literature Review (contd.)
United International University

## Slide 8
Anirvin Sharma, Tanupriya Choudhury, and Praveen Kumar. Health monitoring & management using iot devices in a cloud based framework. In 2018 International Conference on Advances in Computing and Communication Engineering (ICACCE), pages 219-224. IEEE, 2018.
  Three layers: The detecting layer, The transport layer, and The application layer.
  Pulse, blood pressure, oxygen saturation, BMI, ECG signal, Glucose, Body Fat.
  Pulse and SpO2 sensor, BP sensor, weight scale, ECG sensor, Glucometer, EMG sensor, EEG sensor, GSR sensor, temperature sensor DS18B20, ADXL335.
Naina Gupta, Hera Saeed, Sanjana Jha, Manisha Chahande, and Sujata Pandey. Study and implementation of iot based smart healthcare system. In 2017 International Conference on Trends in Electronics and Informatics (ICEI), pages 541-546. IEEE, 2017.
  Smart heart disease monitoring system.
  Pulse sensor, GSM module, Atmega328 Microcontroller, Arduino Uno and temperature sensor LM35.
  Neural network machine learning algorithm.
Literature Review (contd.)
United International University

## Slide 9
No. | Paper Title | Algo | Device | Area
01 | The IoT-based heart disease monitoring system for pervasive healthcare service (Ref-1) | N/A | SpO2 Sensor device, Smart phone | Heart disease monitoring
02 | IoT based Heart Attack Detection, Heart Rate and Temperature Monitor (Ref-2) | N/A | Arduino Uno, Heart rate sensor, Wi-Fi Module ESP8266, LM35 sensor | Heart and Temperature monitoring
03 | Internet of Things (IoT) based smart health care system (Ref-3) | N/A | Arduino Fio, Temperature sensor, Pulse rate sensor, blood pressure sensor | Temperature and Blood Pressure
04 | IoT based Generic Health Care System (Ref-4) | N/A | Blood Suger sensor, Heart pressure sensor, Weight scale sensor | Integrated Cloud computing with IoT
05 | Health Monitoring &amp; Management using IoT devices in a Cloud Based Framework (Ref-5) | N/A | DS18B20, pulse sensor, ADXL335, AD8232 | Body temperature, pulse rate, body position, ECG
06 | Study and Implementation of IOT based Smart Healthcare System (Ref6) | Neural Network | Pulse sensor, GSM module Atmega328 micro controller, Arduino Uno, LM35 | Heart
07 | An Implementation of IoT for Healthcare (Ref-7) | N/A | Intel Galileo Generation 2, XB24-B XBee S2 Modules, LM35 Temperature Sensor | Body temperature
08 | AN IOT BASED PATIENT MONITORING SYSTEM USING RASPBERRY PI (Ref-8) | N/A | Raspberry Pi, Temperature sensor, Pulse rate sensor, MMA7260QT, Thermistor | Pulse rate, Temperature, respiration rate, Movement
09 | A REVIEW PAPER ON SMART HEALTH CARE SYSTEM USING INTERNET OF THINGS (Ref-9) | N/A | DS18B20 temperature sensor, heartbeat sensor, arduino Uno, Wi-Fi module | Body temperature, Heart beat
10 | Smart Health Care System Using Internet of Things (Ref-10) | N/A | Temperature sensor, Hear rate sensor, GPS | Body temperature, ECG, blood pressure, Oxygen Level
11 | Smart Medicine and Physical Health System Using IoT (Ref-11) | N/A | N/A | Ontology based automating design methodology
12 | A Custom Internet of Things Healthcare System (Ref-12) | N/A | Pulse, SpO2, GSR, Sphygmomanometer, accelerometer, EMG | Heart beat, Movement, body temperature, Oxygen level
Literature Review (contd.)
United International University

## Slide 10
Proposed System Architecture
Methodology
United International University
Develop a device that is used to collect data from the patient body.
Sensors collect the data and send it to local server through microcontroller.
To specify the information of a patient, we will use a gateway.
Develop a web application.
Figure 2: Block Diagram of a system architecture
Figure 2: System Architecture

## Slide 11
Software Requirements
Open Source.
Support C and C++.
Figure 3: Arduino IDE
Methodology (contd.)
United International University
Figure 4: Atom IDE
Open Source.
Support for plug-ins written in Node.js, python.

## Slide 12
Hardware Requirements
Figure 5: Temperature Sensor
Figure 8: Node MCU Microcontroller
Methodology (contd.)
United International University
Figure 7: Oximeter Sensor
Figure 6: Pulse Sensor

## Slide 13
Develop a monitoring system to observe the patient’s data in hospital.
Record the continuous evaluation of patient health condition.
Inform the assigned doctor & relatives automatically through a web application when a patient’s condition is unstable.
Expected Outcome
United International University

## Slide 14
Pictures of our System
Implementation
United International University
Figure 9: Login Credential

## Slide 15
Implementation (contd.)
United International University
Figure 10: Home Page
Doctor Registration
Patient Registration
Ambulance Registration
Cardiology Emergency Monitoring
Neurology Emergency Monitoring
Gynecology Emergency Monitoring
Orthopedics Emergency Monitoring
Cardiology
Neurology
Gynecology
Orthopedics
Pictures of our System

## Slide 16
Implementation (contd.)
United International University
Pictures of our System
Figure 11: Patient List
Figure 12: Individual Department

## Slide 17
Implementation (contd.)
United International University
Pictures of our System
Figure 13: Patient Details

## Slide 18
Implementation (contd.)
United International University
Pictures of our System
Figure 14: Doctor List
Figure 15: Individual Department

## Slide 19
Implementation (contd.)
United International University
Pictures of our System
Figure 16: Doctor Details

## Slide 20
Implementation (contd.)
United International University
Pictures of our System
Figure 17: Algorithm for Emergency Monitoring

## Slide 21
Implementation (contd.)
United International University
Pictures of our System
Figure 18: Emergency Monitoring
Figure 19: Normal Monitoring

## Slide 22
Implementation (contd.)
United International University
Pictures of our System
Figure 20: Emergency Alert
Figure 21: Available Ambulance
Figure 22: Ambulance Details
Figure 23: Ambulance Booking

## Slide 23
Implementation (contd.)
United International University
Pictures of our System
Figure 24: Doctor’s Prescription

## Slide 24
Implementation (contd.)
United International University
Pictures of our System
Figure 25: Home Monitoring

## Slide 25
Implementation (contd.)
United International University
Figure 26: Entity Relationship Diagram
Pictures of our Database

## Slide 26
Implementation (contd.)
United International University
Figure 27: Django Administration
Pictures of our Database

## Slide 27
Standards:
  Software Standard
    The Linux Standard Based(LSB).
    International Organization for Standardization(ISO).
  Hardware Standard
    IEEE 1451.
  Communication Standard
    IEEE 802.11.
  Programming Language
    Python, C, C++.
Standards and Design Constraints
United International University
Constraints:
  Sustainability.
  Manufacturability.
Impacts:
  Environmental Impacts.
  Social Impacts.
  Ethical Impacts.
  Political Impacts.

## Slide 28: Plan - Trimester 1
Problem Selection and Group Discussion
Literature Review
Presentation & Latex Overview
Report Writting
Problem Specification
Mid Week
Defining Methodology
Prepare for Pre-defence
Week
1-2
Week
7
Week
8-9
Week 4-6
Week
3
Week
10
Week
12
Week
11
Gantt Chart
United International University

## Slide 29: Plan - Trimester 2
Hardware and Software Design
Implementation -
Software
Testing
Final Report
Mid Week
Result Analysis and Finalization
Prepare
for Defence
Week
1-2
Week
7
Week
8
Week
5-6
Week
3-4
Week
9-10
Week
12
Week
11
Implementation -
Hardware
Gantt Chart (contd.)
United International University

## Slide 30
Improve the monitoring of the patient’s health condition.
Fast and real-time tracking using IoT application for improved healthcare system .
In future, we will improve our project by using more advanced sensors and add more features.
Develop a mobile application.
Use machine learning application.
Improve our system with hospital requirements.
Conclusion and Future Work
United International University

## Slide 31
[1] Chao Li, Xiangpei Hu, and Lili Zhang. The iot-based heart disease monitoring system for pervasive healthcare service. Procedia computer science, 112:2328-2334, 2017.
[2] S Gowrishankar, MY Prachita, and Arvind Prakash. Iot based heart attack detection, heart rate and temperature monitor. International Journal of Computer Applications, 170(5):26-30, 2017.
[3] Vikas Vippalapalli and Snigdha Ananthula. Internet of things (iot) based smart health care system. In 2016 International Conference on Signal Processing, Communication, Power and Embedded System (SCOPES), pages 1229-1233. IEEE, 2016.
[4] JV Alamelu and A Mythili. Design of iot based generic health care system. In 2017 International conference on Microelectronic Devices, Circuits and Systems (ICMDCS), pages 1-4. IEEE, 2017.
[5] Anirvin Sharma, Tanupriya Choudhury, and Praveen Kumar. Health monitoring & management using iot devices in a cloud based framework. In 2018 International Conference on Advances in Computing and Communication Engineering (ICACCE), pages 219-224. IEEE, 2018.
[6] Naina Gupta, Hera Saeed, Sanjana Jha, Manisha Chahande, and Sujata Pandey. Study and implementation of iot based smart healthcare system. In 2017 International Conference on Trends in Electronics and Informatics (ICEI), pages 541-546. IEEE, 2017.
[7] Ravi Kishore Kodali, Govinda Swamy, and Boppana Lakshmi. An implementation of iot for healthcare. In 2015 IEEE Recent Advances in Intelligent Computational Systems (RAICS), pages 411-416. IEEE, 2015.
[8] R Kumar and M Pallikonda Rajasekaran. An iot based patient monitoring system using raspberry pi. In 2016 International Conference on Computing Technologies and Intelligent Data Engineering (ICCTIDE'16), pages 1-4. IEEE, 2016.
[9] K Natarajan, B Prasath, and P Kokila. Smart health care system using internet of things. Journal of Network Communications and Emerging Technologies (JNCET), 6(3), 2016.
[10] Zankhana Mehul Kalarthi. A review paper on smart health care system using internet of things. International Journal of Research in Engineering and Technology, 5(03):8084, 2016.
[11] P Elanthiraiyan, Dr S Babu, et al. Smart medicine and physical health system using Iot. International Journal of Computer Science and Mobile Computing, 4(3):333-338, 2015.
[12] Mirjana Maksimovic, Vladimir Vujovic, and Branko Perisic. A custom internet of things healthcare system. In 2015 10th Iberian Conference on Information Systemsand Technologies (CISTI), pages 1-6. IEEE, 2015.
References
United International University

## Slide 32
[13] Musaed Alhussein, Ghulam Muhammad, M Shamim Hossain, and Syed Umar Amin. Cognitive iot-cloud integration for smart healthcare: case study for epileptic seizure detection and monitoring. Mobile Networks and Applications, 23(6):1624{1635, 2018.
[14] M Shamim Hossain, Ghulam Muhammad, and Atif Alamri. Smart healthcare monitoring: A voice pathology detection paradigm for smart cities. Multimedia Systems, 25(5):565{575, 2019.
[15] Abdul Ahad, Mohammad Tahir, and Kok-Lim Alvin Yau. 5g-based smart healthcare network: architecture, taxonomy, challenges and future research directions. IEEE Access, 7:100747{100762, 2019.
[16] Amir-Mohammad Rahmani, Nanda Kumar Thanigaivelan, Tuan Nguyen Gia, Jose Granados, Behailu Negash, Pasi Liljeberg, and Hannu Tenhunen. Smart e-health gateway: Bringing intelligence to internet-of-things based ubiquitous healthcare systems.
In 2015 12th Annual IEEE Consumer Communications and Networking Conference (CCNC), pages 826{834. IEEE, 2015.
[17] Md Golam Rabiul Alam, Md Shirajum Munir, Md Zia Uddin, Mohammed Shamsul Alam, Tri Nguyen Dang, and Choong Seon Hong. Edge-of-things computing framework for cost-eective provisioning of healthcare data. Journal of Parallel and
Distributed Computing, 123:54{60, 2019.
[18] Sukhpal Singh Gill, Rajesh Chand Arya, Gurpreet Singh Wander, and Rajkumar Buyya. Fog-based smart healthcare as a big data and cloud service for heart patients using iot. In International Conference on Intelligent Data Communication Technologies and Internet of Things, pages 1376{1383. Springer, 2018.
[19] Prabal Verma and Sandeep K Sood. Fog assisted-iot enabled patient health monitoring in smart homes. IEEE Internet of Things Journal, 5(3):1789{1796, 2018.
[20] Ziad Obermeyer, Jasmeet K Samra, and Sendhil Mullainathan. Individual dierences in normal body temperature: longitudinal big data analysis of patient records. Bmj, 359, 2017.
[21] Colin Hester. Celsius to fahrenheit|quick and dirty. Journal of Chemical Education, 72(11):1026, 1995.
[22] Robert Avram, Georey H Tison, Kirstin Aschbacher, Peter Kuhar, Eric Vittingho, Michael Butzner, Ryan Runge, Nancy Wu, Mark J Pletcher, Gregory M Marcus, et al. Real-world heart rate norms in the health eheart study. NPJ digital medicine,
2(1):1{10, 2019.
[23] Gozde Ates and Kemal Polat. Measuring of oxygen saturation using pulse oximeter based on fuzzy logic. In 2012 IEEE International Symposium on Medical Measurements and Applications Proceedings, pages 1{6. IEEE, 2012.
References
United International University

## Slide 33
United International University